## Slide 1: Amazon Web Services F1 Instance
By,
Medini J. Aradhya
Reconfigurable Computing

## Slide 2: Description :
The amazon web services cloud platform is compatible with existing FPGA algorithms hence makes it a versatile open source platform for accelerated computing.
Xilinx FPGAs are available in the Amazon Elastic Compute Cloud (Amazon EC2) F1 instances.
F1 instances are designed to accelerate data center workloads.
With F1 instances you can: Quickly deploy custom hardware acceleration  Enjoy predictable performance with dedicated FPGAs  Use your existing FPGA algorithms
Notes: medini

## Slide 3: Xilinx Cloud Acceleration Tool on AWS
Amazon Web Services offers the Xilinx SDAccel ™ Development Environment for cloud acceleration.
SDAccel empowers hardware designers to easily deploy their RTL designs in the F1 instance.
It also automates the acceleration of code written in C, C++ or OpenCL by building application-specific accelerators on the F1 instances.
Notes: anushka

## Slide 4: Getting Started with SDAccel :
Prerequisites
Create, Configure, Test
AWS-F1 and SDAccel
Install and run SDAccel.
https://www.xilinx.com/products/design-tools/acceleration-zone/aws.html#overview
Notes: anushka

## Slide 5: Prerequisites
Create AWS Account (https://aws.amazon.com/)
Select region from console ( Make sure to keep the region uniform throughout your use of AWS.
Create S3 (storage) Bucket. An Amazon S3 bucket is required to run the Amazon FPGA Image (AFI) creation service.
The bucket will contain a tar file and logs which are generated from the Amazon FPGA Image (AFI) creation service. (namely Design Checkpoints and Logs)
Notes: Medini

## Slide 6: Prerequisites
Prepare your Private Connection Keys
EC2>Networks and Security> KeyPairs> Create Key Pair
For windows convert the generated “.pem” file to “.ppk” file using PuttyGen
Your private key is now in the correct format for use with PuTTY to connect to an AWS EC2 instance.
Request access to AWS –F1 instance EC2Request>Service Limit Increase form> f1.2xlarge or 16xlarge instance type.
Notes: Medini

## Slide 8: Create, Configure and Testing – AWS-F1
EC2 dashboard>Launch Instance> AMI (Amazon Machine Image)>FPGA Developer AMI>select f1.2xlarge instance.
Next: configure instance details>Add storage (default)>Add tags(default)>Configure Security Group.
Under security group Add Rule (in addition of SSH(default) : Type: RDP Protocol: TCP (default value) Port Range: 3389 (default value) Source: Custom - 0.0.0.0/0
Review and Launch Instance ( Make note of IPv4 Public DNS and Public IP address of the instance.)
Notes: Medini

## Slide 9: Create, Configure and Testing – AWS-F1
Connecting the Instance with the Remote Desktop Client :  Use PuTTy from command prompt to connect : putty -i <AWS key pairs.ppk> -ssh centos@<public IP address of EC2 instance> 22
<AWS key pairs> is the full path to the .pem (SSH) or .ppk (PuTTY) file containing the key pairs.
<public DNS of EC2 instance> is the Public DNS of the instance.
User name: centos ; connection type: SSH ; Port :22.
You are now connected to the EC2 Instance.
Notes: Medini

## Slide 10: Create, Configure and Testing – AWS-F1
Set up the GUI on the Instance :  The FPGA Developer AMI does not include a GUI desktop application  Install the Gnome window manager and start remote desktop protocol (RDP) services to allow remote desktop connections. “source <(curl -s https://s3.amazonaws.com/aws-fpga-developer-ami/1.5.0/Scripts/setup_gui.sh)”  User: Centos & Password: Generated by above script. you will need to reboot your instance before connecting to the RDP client Machine. (IMPORTANT: Set your RDP client to use 24-bit for color depth & in RDP client, enter the IPv4 Public IP)
You are now connected to the instance running Centos 7 and the FPGA Developer AMI.
Notes: Medini

## Slide 11: Create, Configure and Testing – AWS-F1
Configure the Instance for working with SDAccel:  In the RDP Client open a terminal.  Configure AWS CLI : $ aws configure AWS Access Key ID [None]: <your access key> AWS Secret Access Key [None]: <your secret key> Default region name [None]: <your AWS region > Default output format [None]: json
 Before Configuring we must go to IAM > Create Group > add Users to the group > Set permissions ( under attach policy).  The above credentials can be found in AMI>Users>select user> credentials> create access key >(download the file containing the details)  Rest of the info : Region Name can be found in EC2 instance dashboard under description.
Notes: Medini

## Slide 12: Create, Configure and Testing – AWS-F1
Conti….. User: Centos & Password: Generated by above script. you will need to reboot your instance before connecting to the RDP client Machine. (IMPORTANT: Set your RDP client to use 24-bit for color depth & in RDP client, enter the IPv4 Public IP) You are now connected to the instance running Centos 7 and the FPGA Developer AMI.
Configure the SDAccel Environment :  Execute the following commands from the command line of the instance terminal: git clone https://github.com/aws/aws-fpga.git $AWS_FPGA_REPO_DIR cd $AWS_FPGA_REPO_DIR source sdaccel_setup.sh (first time you run it, the script will download the platform and compile the runtime and drivers. Subsequent runs are much faster. You must source sdaccel_setup.sh each time you open a new terminal)
Notes: Medini

## Slide 13: Testing & Demonstration – AWS
Connected to the RDP Client where the instance is running Centos 7 and the FPGA Developer AMI.
Notes: Medini

## Slide 14: Testing & Demonstration – AWS
Notes: Medini

## Slide 16: SDAccel – Download and Install.
The SDAccel emulation flows allows testing, profiling, and debugging the application before deploying it on F1.
https://www.xilinx.com/support/download/index.html/content/xilinx/en/downloadNav/sdaccel-development-environment.html
Download the web installer for Linux as the RTL Kernel is supported only on Linux environments.
Make it an executable using chmod and run the installer and follow the prompts.
Upgrade the Vivado Design suite to SD Accel development environment.
Notes: Medini

## Slide 18: Set Up the Alveo U200 Accelerator Card
Download the Xilinx Runtime and Deployment and Development Shell to be able to interface with AWS F1. Then follow the Getting Started Guide.
https://www.xilinx.com/products/boards-and-kits/alveo/u200.html#gettingStarted
This will make the U200 platform available on the Local SDx suite.
Notes: Medini

## Slide 21
Notes: Medini

## Slide 22
Notes: Anushka

## Slide 23
Notes: Anushka